## Slide 1
Patent No. JP 5211056
（Japan Patent）
MJ3-10-SE
～ MJ3-SE ～
(Drying Adjustment System)
You can retrofit to existing machines!
Because
we are MATSUI !

## Slide 2
When a dryer was running at
full power (max. dry air flow rate)
even while a molding machine stopped,
Discharge Valve
Honeycomb Rotor―
Regeneration Heater
Regeneration
Blower
After Cooler
Drying Blower
Conveying Blower
Drying Hopper
Drying
Heater
Molding Machine
Preparation time got longer
One less
operating machine than usual
Stopped due to
maintenance
The energy was left over
in such a case.
But MJ3-SE is
different!
Note 1: The device configuration flow is for MJ3-10.
The device configuration flow varies depending on
the model, but a bypass circuit can be installed in
dehumidified dry air circulation circuit in any model.
Note 2: Heat radiation from after cooler to the room is only for
MJ3-10 to 75 (air cooled).
MJ3-100 to 300 (water cooling) exhaust heat to cooling water.
Discharge Valve
Honeycomb
Rotor
Drying Blower
After Cooler
Regeneration Blower
Regeneration Heater
Drying
Heater
Material Tank
Drying
Hopper
Heat Radiation
Proper
Drying
Flow Rate
Adjusting Valve
Proper
Proper air flow rate
Temperature
Sensor
When the exhaust temperature of the drying hopper becomes higher than the set temperature, a part of the circulating drying air is bypassed, then the amount of air flow rate supplied to the drying hopper is reduced.
Molding Machine
Conveying Blower

## Slide 3
Supplying only the required amount of
dry air flow rate reduces
the power consumption of dry heater!
Discharge Valve
Honeycomb
Rotor
Drying Blower
After Cooler
Regeneration Blower
Regeneration Heater
Drying
Heater
Material Tank
Drying
Hopper
Heat Radiation
Flow Rate
Adjusting Valve
Temperature
Sensor
When the exhaust temperature of the drying hopper becomes higher than the set temperature, a part of the circulating drying air is bypassed, then the amount of air flow rate supplied to the drying hopper is reduced.
Molding Machine
Conveying Blower
Note 1: The device configuration flow is for MJ3-10.
The device configuration flow varies depending on
the model, but a bypass circuit can be installed in
dehumidified dry air circulation circuit in any model.
Note 2: Heat radiation from after cooler to the room is only for
MJ3-10 to 75 (air cooled).
MJ3-100 to 300 (water cooling) exhaust heat to cooling water.
Is there no problem with the dew point?
The dew point is stable because no change in air flow rate through honeycomb.
When a dryer was running at full power (max. drying air flow rate)
while a molding machine stopped,
Discharge
Valve
Honeycomb
Rotor―
Regeneration Heater
Regeneration
Blower
After Cooler
Drying Blower
Conveying Blower
Drying
Hopper
Heat Radiation
Overdrying
Drying
Heater
Excessive
air flow rate
- wasting extra heating of the air,
which is irrelevant to temperature rise
of the material, by drying heater.
- excessive temperature rise (overdry)
of the material was caused.
Proper
Drying
Proper air flow rate

## Slide 4
Lower exhaust temperature reduces
air conditioning equipment load and
saves energy!
Note 1: The device configuration flow is for MJ3-10.
The device configuration flow varies depending on
the model, but a bypass circuit can be installed in
dehumidified dry air circulation circuit in any model.
Note 2: Heat radiation from after cooler to the room is only for
MJ3-10 to 75 (air cooled).
MJ3-100 to 300 (water cooling) exhaust heat to cooling water.
Is there no problem with the dew point?
The dew point is stable because no change in air flow rate through honeycomb.
When a dryer is running at full power (max. drying air flow rate)
while a molding machine is stopped,
the excess heat was released
from after cooler to outside
of the machine.
Discharge Valve
Honeycomb
Rotor
Drying Blower
After Cooler
Regeneration Blower
Regeneration Heater
Drying
Heater
Material Tank
Drying
Hopper
Heat Radiation
Flow Rate
Adjusting Valve
Temperature
Sensor
When the exhaust temperature of the drying hopper becomes higher than the set temperature, a part of the circulating drying air is bypassed, then the amount of air flow rate supplied to the drying hopper is reduced.
Molding Machine
Conveying Blower
Proper
Discharge
Valve
Honeycomb
Rotor―
Regeneration Heater
Regeneration
Blower
After Cooler
Drying Blower
Conveying Blower
Drying
Hopper
Heat Radiation
Overdrying
Drying
Heater
Lots of
wasted energy
High
temperature
Proper
Drying

## Slide 5
Discharge Valve
Conveying Blower
Drying Blower
After Cooler
Regeneration
Blower
Regeneration Heater
Drying
Heater
Molding Machine
Material Tank
Drying
Hopper
Heat Radiation
Flow Rate
Adjusting Valve
Dry with an appropriate
air flow rate suitable for
the operating conditions!
When the exhaust temperature is
higher than the set temperature,
decrease the supply amount of
the drying hopper
(increase the bypass flow rate).
When the exhaust temperature is
lower than the set temperature,
increase the supply amount of
the drying hopper
(decrease the bypass flow rate).
Proper
Drying
Proper
Note 1: The device configuration flow is for MJ3-10. The device configuration flow varies depending on the model, but bypass circuit can be installed in dehumidified dry air circulation circuit in any model.
Note 2: Heat radiation from an after cooler to the room is only for MJ3-10 to 75 (air cooled). MJ3-100 to 300 (water cooling) exhaust heat to cooling water.
More Details!
What happens if the exhaust temperature falls below the set temperature?
Drying
Heater
Conveying Blower
Drying Blower
After Cooler
Regeneration
Blower
Regeneration Heater
Molding Machine
Material Tank
Drying
Hopper
Heat Radiation
Overdrying
Drying
Heater
Conveying Blower
Drying Blower
After Cooler
Regeneration
Blower
Regeneration Heater
Molding Machine
Material Tank
Heat Radiation
Insufficient
drying
Drying
Hopper
Excessive
air flow rate
Insufficient
air flow rate
Lots of
wasted energy
High
temperature
Proper
air flow rate

## Slide 6
MATSUI technology
also here!
Patent No. JP 5130338
Good
Reabsorption of the material after drying and
temperature drop are reduced by
filling the material conveying line with dehumidified dry air!
What does “filling the material conveying
line with dehumidified dry air” mean?
A part of the dehumidified dry air,
supplied to the drying hopper,
flows into the material
conveying pipeline through a gap
between the discharge port.
Gap
～Other expected effects!～
Diagonal mechanism
allows materials to be
discharged smoothly!
Prevent
jammed!
Powder pressure
on the valve body is
reduced and the valve
body moves smoothly!
More Details!
Make a gap between the discharge port and the closed discharge valve to prevent material from falling.
Molding Machine
Material Tank
Drying
Heater
Drying
Hopper
Discharge Valve
Drying Blower
Conveying Blower
After Cooler
Regeneration Heater
Regeneration
Blower
Dehumidified Dry Air Circulation Circuit
The discharge pipe is inclined downward.
Material Conveying Pipeline
Honeycomb
Rotor

## Slide 7
Good
Supplying only the required
amount of dry air flow rate reduces
the power consumption of dry heater!
MJ3-SE (Drying Adjustment System) is
MATSUI‘s technology that other companies cannot do.
Good
Lower exhaust temperature reduces
air conditioning equipment load and
saves energy!
MJ3-10-SE
You can retrofit to
existing machines!
Because
we are MATSUI !
Discharge Valve
Honeycomb
Rotor
Drying Blower
After Cooler
Regeneration Blower
Regeneration Heater
Drying
Heater
Material Tank
Drying
Hopper
Heat Radiation
Proper
Drying
Flow Rate
Adjusting Valve
Proper
Proper air flow rate
Temperature
Sensor
When the exhaust temperature of the drying hopper becomes higher than the set temperature, a part of the circulating drying air is bypassed, then the amount of air flow rate supplied to the drying hopper is reduced.
Molding Machine
Conveying Blower
(Patent No. JP 5211056）

## Slide 8
Good ideas
addition to
patented technology
MJ3-SE (Drying adjustment system) not only adjust dry air flow rate but also
adjust the regenerated air flow rate to reduce unnecessary energy consumption of the dryer.
Regenerate with an appropriate
air flow rate suitable for
the operating conditions!
Drying Heater
Conveying Blower
Drying Blower
After Cooler
Regeneration Blower
Regeneration
Heater
Molding Machine
Material Tank
Drying
Hopper
Over
regeneration
Drying Heater
Conveying Blower
Drying Blower
After Cooler
Regeneration Blower
Regeneration
Heater
Molding Machine
Material Tank
Insufficient
reproduction
Drying
Hopper
Flow Rate
Adjusting Valve
Flow Rate
Adjusting Valve
Flow Rate
Adjusting Valve
Flow Rate
Adjusting Valve
Excessive
air flow rate
Lots of
wasted energy
High
temperature
Temperature
Sensor
Temperature
Sensor
Discharge Valve
Discharge Valve
Insufficient
air flow rate
When the honeycomb
regeneration exhaust
temperature is higher than
the set temperature,
the regeneration air flow rate is
reduced.
When the honeycomb
regeneration exhaust
temperature is lower than
the set temperature,
the regeneration air flow rate is
increased.
Note: The device configuration flow is for MJ3-10. For MJ3-10 to 150, the supply air flow rate is adjusted by the flow rate adjusting valve installed between regeneration blower and regeneration heater.
For MJ3-200 to 300, the supply air flow rate is adjusted by an inverter installed in the regeneration blower.
Discharge Valve
Conveying Blower
Drying Blower
After Cooler
Regeneration Blower
Regeneration
Heater
Drying Heater
Molding Machine
Material Tank
Drying
Hopper
Flow Rate
Adjusting Valve
Flow Rate
Adjusting Valve
Temperature
Sensor
Proper
Drying
Proper
Proper
air flow rate