## Slide 1
～ MJ5-i ～
MJ5-i-150-J
Because
we are MATSUI !
Patent No. JP 5420375
（ Japan Patent ）

## Slide 2
Existing dehumidifying dryer was ...
- The outside air at room temperature
was taken in and heated by
the regeneration heater
- Honeycomb regeneration heating
exhaust was discharged outside
the machine at high temperature
But MJ5-i is
different!
Drying Blower
Conveying Blower
Cooler
Drying
Heater
Discharge Valve
Honeycomb
Rotor
Regeneration
Blower
Drying
Hopper
To molding machine
From
material
tank
From outside air
To outside machine
(Waste Heat)
Regeneration Heater
Molding Machine
Material Tank
Drying
Heater
Drying
Hopper
Discharge Valve
Drying Blower
Conveying Blower
Cooler
Honeycomb
Rotor
Regeneration
Heater
Heat Exchanger
Regeneration
Blower
Honeycomb regeneration heating exhaust and honeycomb regeneration cooling exhaust pass through heat exchanger.

## Slide 3
Molding Machine
Material Tank
Drying
Heater
Drying
Hopper
Discharge Valve
Drying Blower
Conveying Blower
Cooler
Honeycomb
Rotor
Regeneration
Heater
Heat Exchanger
Regeneration
Blower
Honeycomb regeneration heating exhaust and honeycomb regeneration cooling exhaust pass through heat exchanger.
Preheat the regeneration heating air with
waste heat to reduce the power consumption
of regeneration heater!
When the outside air at room temperature was
taken in and heated by the regeneration heater,
much energy was required to heat the outside air
at room temperature.
Drying Blower
Conveying Blower
Cooler
Drying
Heater
Discharge Valve
Honeycomb
Rotor
Regeneration
Blower
Drying
Hopper
To molding machine
From
material
tank
From outside air
To outside machine
(Waste Heat)
Regeneration Heater

## Slide 4
Molding Machine
Material Tank
Drying
Heater
Drying
Hopper
Discharge Valve
Drying Blower
Conveying Blower
Cooler
Honeycomb
Rotor
Regeneration
Heater
Heat Exchanger
Regeneration
Blower
Honeycomb regeneration heating exhaust and honeycomb regeneration cooling exhaust pass through heat exchanger.
Drying Blower
Conveying Blower
Cooler
Drying
Heater
Discharge Valve
Honeycomb
Rotor
Regeneration
Blower
Drying
Hopper
To molding machine
From
material
tank
From outside air
To outside machine
(Waste Heat)
Regeneration Heater
Lower exhaust temperature reduces
air conditioning equipment load and saves energy!
When the honeycomb regeneration heating exhaust
was discharged outside the machine at high temperature,
the air conditioning equipment was overloaded due to
the high exhaust temperature.

## Slide 5
- What does “preheat the regeneration heating air with waste heat” mean?
- Why does the exhaust temperature drop?
High-temperature honeycomb regeneration heating exhaust and honeycomb regeneration
cooling exhaust exchange heat with low-temperature outside air, then the temperature of
the regeneration heating air is preliminarily raised in temperature.
Molding Machine
Material Tank
Drying
Heater
Drying
Hopper
Discharge Valve
Drying Blower
Conveying Blower
Cooler
Honeycomb
Rotor
Regeneration
Heater
Heat
Exchanger
Regeneration
Blower
Heat exchange is
the transfer of heat energy from high-temperature fluid
to low-temperature fluid.
(The heat energy has
the property of moving
from high to low)
■: Dehumidification zone
■: Regeneration cooling zone
■: Regeneration heating zone
Adsorb moisture with honeycomb
Water evaporation
from honeycomb
Cool honeycomb to the proper temperature for dehumidification
Honeycomb regeneration
heating exhaust
Honeycomb regeneration
cooling exhaust
Exhaust temperature
to outside of
the machine drops!
The temperature
introduced to
the regeneration heater rises!
Honeycomb
regeneration
heating exhaust
(100-140℃)
Honeycomb
regeneration
cooling exhaust
(150-190℃)
Regeneration exhaust
(Approx. 80℃)
Cooling exhaust
Outside air
(20-35℃)
Regeneration heating air
(Approx. 80℃)
Heat Exchanger
No water transfer!
Mechanism of Honeycomb
Mechanism of Heat Exchanger
[Reference]
Overall heat transfer coefficient 33.0 W/(m2・K) (Actual value)
(28.4 kcal/(m2・h・K))
Heat collection rate 67 % (Actual value)
More Details!

## Slide 6
MATSUI technology
also here!
Patent No. JP 5130338
Make a gap between the discharge port and the closed discharge valve to prevent material from falling.
The discharge pipe is inclined downward.
What does “filling the material conveying
line with dehumidified dry air” mean?
A part of the dehumidified dry air,
supplied to the drying hopper,
flows into the material
conveying pipeline through a gap
between the discharge port.
Gap
～Other expected effects!～
Diagonal mechanism
allows materials to be
discharged smoothly!
Prevent
jammed!
Powder pressure
on the valve body is
reduced and the valve
body moves smoothly!
[Reference] When APH is used for the collector, the dew point is -30 to -40 ℃ (actual value)
The material did not reabsorb at in-house test using PET.
Material Tank
Drying
Heater
Drying
Hopper
Discharge Valve
Drying Blower
Conveying Blower
Cooler
Honeycomb
Rotor
Regeneration
Heater
Heat Exchanger
Regeneration
Blower
Dehumidified Dry Air Circulation Circuit
Material Conveying Pipeline
Molding Machine
More Details!
Good
Reabsorption of the material after drying and
temperature drop are reduced by
filling the material conveying line with dehumidified dry air!

## Slide 7
MJ5-i-150-J
Good
Preheat the regeneration heating air with
waste heat to reduce the power consumption
of regeneration heater!
Good
Lower exhaust temperature reduces
air conditioning equipment load and
saves energy!
The energy-saving technology of MJ5-i is
MATSUI‘s technology that other companies cannot do.
(Patent No. JP 5420375)
Because
we are MATSUI !
Molding Machine
Material Tank
Drying
Heater
Drying
Hopper
Discharge Valve
Drying Blower
Conveying Blower
Cooler
Honeycomb
Rotor
Regeneration
Heater
Heat Exchanger
Regeneration
Blower
Honeycomb regeneration heating exhaust and honeycomb regeneration cooling exhaust pass through heat exchanger.